## Slide 1: Paper reading: Pseudo lidar for 3D object detection
Houpu Yao
2019.10.25
Notes: Background
Algorithm: Pseudo lidar (PL)
Algorithm: Pseudo lidar++ (PL++)
Discussions

## Slide 2: Background
What is pseudo lidar?
  Extract the geometry information captured by camera sensors and transform it into point clouds representation
Why pseudo lidar?
  Lidar: Cost too high, but accurate 3D bounding box detection
  Camera: lower cost, but not good at 3d bounding box detection
  Pseudo lidar: much lower cost than Lidar, better performance than camera
Notes: First, local patches on 2D images are only coherent physically if they are entirely contained in a single object.
Second, objects that occur at multiple depths project to different scales in the depth map.

## Slide 3: Object detection with PL
Wang, Yan, et al. “ Pseudo-lidar from visual depth estimation: Bridging the gap in 3d object detection for autonomous driving." Proceedings of the IEEE Conference on Computer Vision and Pattern Recognition. 2019.
Geometry based
Deep learning based
VAOD
Frustum PointNet
PointPillars
….
Disparity map
Geometric transformations
Notes: The whole pipeline is trained with kitti dataset. Since the maximum depth in the dataset is 70m, that is the upper limit.

## Slide 4: Object detection with PL
Disparity estimation – with stereo geometry based approach
Stereo camera model:
http://www.cs.toronto.edu/~fidler/teaching/2015/CSC420.html
http://www.cs.toronto.edu/~fidler/teaching/2015/CSC420.html
http://www.cs.toronto.edu/~fidler/teaching/2015/CSC420.html
Template matching for correspondence:
Left image
Right image
How similar?
Error in rectification
Error in template matching
plane
Notes: Question: how to find Epipolar Lines, with fundamental matrix
So far, each left image patch has been matched independently along the right epipolar line. This can lead to errors. We would like to enforce some consistency among matches in the same row (scanline).

## Slide 5: Object detection with PL
disparity estimation – deep learning based approach (PSM-Net)
Disparity level max: 192
Chang, Jia-Ren, and Yong-Sheng Chen. "Pyramid stereo matching network." Proceedings of the IEEE Conference on Computer Vision and Pattern Recognition. 2018.
Construction of cost volume:
Shifting the image by one pixel alone the 3rd dim
Overall network architecture:
Yu, Lidong, et al. "Deep stereo matching with explicit cost aggregation sub-architecture." AAAI. 2018.
Notes: However, current architectures rely on patch-based Siamese networks, lacking the means to exploit context information for finding correspondence in ill posed regions.
In a typical labeling approach, the input data is used to construct a three-dimensional cost volume, which stores the costs for choosing a label l (i.e. disparities in stereo) at image coordinates x and y. For stereo, these costs are given by pixel-wise correlation (e.g. absolute differences of the intensities) between corresponding pixels.
a three-dimensional cost volume is constructed by computing the per-pixel matching costs at all possible disparity levels.
Therefore, doing a so�-max gives a probability distribution over possible values of disparity. But they don't train this with a classification loss: because some mis-classifications are worse than others ! (d=5 instead of 4 is better than d=25 instead of 4)

## Slide 6: Qualitative results of pseudo lidar
Distance: 40m
Distance: 35m
Notes: 1. Looks good in general
2. distortion

## Slide 7: Quantitative results of pseudo lidar
Observations:
1. Pseudo lidar increased object detection accuracy by huge margin
2: object detection based on single image is performing much worse than stereo
3: object detection with pseudo lidar is still not comparable to real lidar performance
Precision in object detection:
  3D object detection results on the KITTI validation set
  AP_BEV / AP_3D (in %) of the car category
  Rows in blue denotes result from pseudo lidar
Notes: Other ways to estimate depth image from single image. These approaches also work in some extend, however, their performance is relatively low.
Lidar: 64 beams from KITTI
MLF CVPR2018 previous SOTA

## Slide 8: Pseudo Lidar ++
Comparison of depth estimation error
Improvements:
Directly estimate depth map
Correction with sparse lidar point cloud
You, Yurong, et al. "Pseudo-LiDAR++: Accurate Depth for 3D Object Detection in Autonomous Driving." arXiv preprint arXiv:1906.06310 (2019)
Network architecture:
Intuition on the high error rate of far away object:
1. Given disparity error, the error in depth increases quadratically with depth
2. Similar to image pixels, the disparity (depth) estimation is quantized
Notes: graph-based depth correction (GDC)
Code not released yet

## Slide 9: Quantitative results of pseudo lidar ++
Precision in object detection:
  Rows in blue denotes result from pseudo lidar++
  Input source: M(Mono), S (Stereo), L# (4-beam lidar), L(64-beam lidar)
Notes: 4 beams lidar + 2 camera: $0.8k
64 beams lidar: $75k
Current best: 79.79%
3D object detection results on KITTI validation. We report APBEV / AP3D (in %) of the car category, corresponding to average precision of the bird’s-eye view and 3D object detection. We arrange methods according to the input signals: M for monocular images, S for stereo images, L for 64-beam LiDAR, and L# for sparse 4-beam LiDAR. PL stands for PSEUDO-LIDAR. Our PSEUDO-LIDAR ++ (PL++) with enhanced depth estimation — SDN and GDC— are in blue. Methods with 64-beam LiDAR are in gray. Best viewed in color.

## Slide 10: Take away points
Three steps of 3D detection based on pseudo lidar:
  Estimate disparity with neural network
  Obtain pseudo lidar point cloud from disparity map based on geometry relationship
  Perform 3D object detection
Advantages:
  The cost is much lower than a real Lidar
  Achieved state-of-the-art performance in image-based 3D bounding box detection
  Existing work on disparity (depth) estimation and 3D object detection can be directly used
Drawbacks:
  Whole workflow takes ~1s
  Low accuracy far away objects

## Slide 11: Summary
Current limitations
Lower resolution
Distortion for far away objects
Future directions
Use much higher resolution image ( current 0.4M pixel)
Incorporate recent depth estimation models: Anynet Madnet
Notes: Training data can be easily obtained from simulators!!
Associate color to the point cloud
  E.g. green points usually corresponds to trees
  Use narrow forward camera
  Larger set of deeper depth image

## Slide 12: Summary
Velodyne VLS-128
  2.4M points per second, 300m, 10Hz
  That is 667 points per angle @ 10 hz
Tesla narrow forward camera
  1280×960, 250m, 30hz, 35 FOV
  That is 35k points per angle @ 30hz

## Slide 13: Future directions, cont’d
Combination with lane detection:
images
depth estimation
3D bbox detection
pseudo point cloud generation
Filtering
(project to 2D)
segmentation
camera input
lane detection
focus on the far end of the lane
Notes: Alpha puck

## Slide 14
Weng, Xinshuo, and Kris Kitani. "Monocular 3D Object Detection with Pseudo-LiDAR Point Cloud." arXiv preprint arXiv:1903.09847 (2019).

## Slide 15: Real-Time Semantic Stereo Matching
Notes: Both segmentation and disparity are fully computed only at the lowest resolution and progressively refined through the higher resolution residual stages

## Slide 16
Yang, Guorun, et al. "DrivingStereo: A Large-Scale Dataset for Stereo Matching in Autonomous Driving Scenarios." Proceedings of the IEEE Conference on Computer Vision and Pattern Recognition. 2019.